H(z) = {b_0 + b_1 z^-1 + b_2 z^-2} over {1 + a_1 z^-1 + a_2 z^-2}
BIQUAD FILTER

Equalizer is constructed out of cascaded biquad filters. Biquad filter is the most common 2nd order IIR filter. It can be implemented in several forms. Following is a performance report of these forms, considering mainly precision issues.
Implemented EQ has 10 bands. Low-pass, high-pass, peaking, low shelf, high shelf filter types are available. Following parameters are available: cutoff frequency, damping factor (except LPF, HPF), Q.

DIRECT FORM I

Implementation has the following difference equation:

yn = b0xn + b1xn-1 + b2xn-2 – a1yn-1 – a2yn-2

Here b coefficients determine zeroes, a – poles of the filter. Four state variables (x – feed forward, y – feedback) are required to implement delay units.
In fixed point realization Q31 input should be scaled to Q30 to avoid overflow on loud signals, coefficients are in Q31 format, and double length accumulator is used, therefore, a quantization is required before output. Error feedback (noise shaping) is advised to improve precision. Calculating specific types of filter, peaking, for instance, one may get coefficients that are impossible to store in Q31 format. To solve this, normalization should be applied. From available filter types it has been found, that the biggest coefficient can evaluate to 8, so every coefficient is dived by this number, and later is being compensated in processing.

DIRECT FORM II

Implementation has the following difference equation:

 wn = xn - a1yn-1- a2yn-2
yn = b0xn + b1wn-1 + b2wn-2

Where wn is a state variable. Implementing this form in floating point a problem can be encountered. If poles and zeroes are located too close to unit circle, state variable can grow fast. Adding small input value, to rather big state variable, reduces the bits to represent mantissa, due to big ratio between two numbers. The result is heavily quantized output signal.
Same issue results in overflow in fixed point arithmetic. Increasing headroom can help. It has been found, that a headroom of 3 bits, allows a LPF to operate normally only on frequencies above 10 kHz on smallest Q. For range 20..20000 Hz, 20 bits of headroom is required, which results in huge noise floor. Therefore this form is not recommended for use.

DIRECT FORM I TRANSPOSED
Implementation has the following difference equation:

 x0 = xn + yn-1	xn-1 = b1x0 + xn-2	yn-1 = -a1x0 + yn-2
 yn = b0 x0 + xn-1	xn-2 = b2x0	yn-2 = -a2x0

Where x, y are state variables. This form has the same issue concerning state variables as a direct form II and is not recommended to use.

DIRECT FORM II TRANSPOSED

Implementation has the following difference equation:

 yn = b0xn + xn-1
        xn-1 = b1xn – a1yn + xn-2
  xn-2 = b2xn – a2yn

Where xn is a state variable. In these form poles and zeroes are combined in a way, eliminating problem, mentioned in previous two forms.

TEST RESULTS
In order to choose the best form, a series of tests has been made.
A test signal is a sine logarithmic chirp, with frequency swept from 1 to 24000 Hz, with 0 dB amplitude.
Having encountered a problem, mentioned above, two forms (Direct Form II, Direct Form I transposed) are not intended to use.
A corrupted resulting signal is shown below. Followed by an absolute error graph. Peaking filter with 10 Hz cutoff frequency, 10 dB damping factor, and Q = 10, is used for this test.

Resulting waveform (cropped)

Absolute error graph

Following tests were aimed to find the best solution for floating point and fixed point realizations between Direct Form I and Direct Form II transposed. As a criteria RMSE has been calculated. As a true value, a double precision processing result is taken. All types of filters has been tested with various parameters. Here are presented only few demonstrative plots, because the differ slightly, depending on parameters.

CONCLUSION

On floating point arithmetic a small increase in precision is seen in Direct Form II transposed. Fixed point realizations show better results in Direct Form I.